## Slide 1: Wireless Based Positioning
Project in Wireless Communication

## Slide 2: Wireless Based Positioning
Adrien Anxionnat
Baptiste Cavarec
Irlon Santos
Navneet Agrawal
Raees Kizhakkumkara Muhamad
Yuqi Zhang

## Slide 3: Positioning Systems
Growing interest in positioning systems
Ultra Wide Band
DecaWave EVB1000

## Slide 4: Setup

## Slide 5: Ranging
Time of Flight
Two-way Ranging
Symmetric Two-way Ranging
Protocol

## Slide 6: Positioning
Trilateration
Static vs Dynamic Positioning
We assume the error in the measurement as Additive White Gaussian Noise

## Slide 7: Static Positioning
The algorithm is derived from a quadratic cost function basis defined over the measurements and using a non-linear least squares estimation to estimate the position
We have to use all measurements till the time to estimate our position.
We avoid using a batch method for computational reasons
Implemented algorithm is recursive and involves a two step approach

## Slide 8: Static Positioning –Two Stage Approach
The two stage approach works by splitting the cost function minimization problem into two steps
The first step is a linear step wherein we estimate a non-linear combination of the parameter such that the measurement is linear with respect to the combination
The linear first step is solved recursively and optimally using a Kalman filter
The first step estimate is fed into an iterative Gauss Newton algorithm to perform a non-linear least squares fit

## Slide 9: Dynamic Positioning
We implemented dynamic positioning using an Extended Kalman Filter
In Extended Kalman Filter we have a state-space model and a measurement model
We model the state(position and velocity) of the tag and includes its position and velocities in the three co-ordinates axes in the state space model
We model the distance equations of the tag from the anchors in the measurement model

## Slide 10: Dynamic Positioning – Extended Kalman Filter
The extended Kalman filter can accept both non-linear state transformations and measurement models unlike the linear Kalman filter
It works by linearizing the model about a working point.
Extended Kalman filter is the ‘defacto’ standard in navigation and GPS systems.

## Slide 11: Results
Parameter estimation
Results before correction
Results after correction

## Slide 12: Results- Parameter estimation

## Slide 13: Results- Parameter estimation

## Slide 14: Results- Parameter estimation

## Slide 15: Results- Parameter estimation

## Slide 16: Results-Results before correction

## Slide 17: Results-Results after correction

## Slide 20: Sources of Error
Clock unsynchronization
Environment

## Slide 21: Sources of Error- Clock

## Slide 22: Sources of Error- Environment

## Slide 23: Sources of Error- Environment

## Slide 24: Sources of Error- Environment

## Slide 25: Sources of Error- Environment

## Slide 26: Conclusion
Project Objectives
  Centimeter accuracy
  Two way and Symmetric two way ranging
  Static and dynamic positioning
Learnings
  Ranging protocols
  Position estimation – estimation theory
  Sources of error
  Project/Team management