## Slide 1: Research & Development
Roberto Roverso
Thursday 25 April 13

## Slide 2: The company
11 Employees
Different Background
  Researchers (2 Professors, 1 Ph.D. Student and 2 Research Engineers)
  Developers (2 Senior and 2 Junior)
  Management (2)
Located in Stockholm
Specialized in scalable systems based on Peer-To-Peer

## Slide 3: The product
Peer-To-Peer Live Streaming Software
  Greatly diminishes bandwidth consumption
  at the distribution point (CDN) and enables corporate multicast

## Slide 4: The numbers
Proxy which sits between CDN and the local player
~80.000 installations in corporate networks
~30.000 WAN installations
  7000 concurrent users
Notes: Since when?

## Slide 5: Live Streaming
Definition:
  “The process of broadcasting live media over the Internet”
Content is recorded, encoded and distributed in real-time
A streaming service provides the media to a client using specific control and transport protocols
Distribution of the stream usually happens using a Content Delivery Network (CDN)
CDN

## Slide 6: Protocols
An encoder digitalizes and compresses media as it is recorded:
  Variety of Video codecs (H.264, VP8), Audio codecs (MP3, Vorbis, AAC) and Media Containers (FLV, WebM, ASF or ISMA)
Media delivery and Streaming protocols
  Stateful/Push/VCR-like: ( OLD )
    Implementations: Real Time Session Protocol (RTSP), Microsoft Media Services (MMS), Adobe’s FLV, etc..
    Single bitrate
    UDP-based transport protocols ( RTP and RealNetwork RDT )
  Stateless/Pull/HTTP-based ( NEW STANDARD )
    Implementations: Apple’s HTTP-Live (HLS), Microsoft Smooth Streaming, Adobe HTTP dynamic streaming (HDS)
    multi-bitrate support

## Slide 7: Content Streaming
Streaming Service
  Sufficient computational power to receive, encode, convert and protect the media content
Distribution
  Streaming is demanding in terms of bandwidth consumption
    You Tube: 256Kbit/s with H.264 codec
    HD Stream: >2Mbit/s
  Yet CDN Bandwidth is not expensive
    Volume: 0.7$ per GB
    Scaling is handled automatically
Vs.
Notes: Distribution site?

## Slide 8: The case for P2P live streaming
CDN
The Reach
  CDN cache cannot serve more than the X capacity it was dimensioned for
  Scaling operations are usually slow
Peer-To-Peer can scale the number of viewers using a fraction of CDN capacity
x
X+N
Redirect

## Slide 9
CDN doesn’t help
Bottleneck on the site’s internet link
Multicast complex to configure
Expensive to introduce hardware CDN nodes inside the Sites
The Corporate Live Streaming case
Main Site
gateway
CDN
Secondary
site
Secondary
site
Secondary
site
Notes: - Imagine a company…
- Company Townhall case – CEO speech
- Netwok collapse

## Slide 10: Peer2View streaming chain
CDN

## Slide 11: Business requirements on P2P streaming application
Hard technical requirements dictated by business reasons
  Given a number of viewers, distribution load by contract:
    Average amount (X)
    Max peak value (Y)
  Infrastructural cost (Z)
  Streaming chain cannot be modified
    Streaming Protocol stack must be maintained “as is”
    Deal with implementations of
      Recorders
      Multitude of Streaming servers and players
  Enforce policies according to customer demands
    Access control, locality, radio network politeness
Notes: What are the variables?
What r the constraints

## Slide 12: P2P Live Streaming Challenges
Real-time nature of the service
  Hard deadlines on the delivery of content
Coping with
  Network Congestion
  Limited bandwidth capacity of peers and source
  Churn
  Connectivity constraints between hosts
    Firewalls and Network Address Translation (NAT)
Maintaining
  Low Delay from the source of the content
    Video played n seconds after it was broadcasted
  Locality of content
    Keep overlay traffic inside the same network segment (ISP and/or AS)
Streaming Server
P2P Swarm

## Slide 13: How to build a peer-to-peer software?
Development
Framework
Money and Time
Network Library
Services
Algorithm
Design and Implementation
Testing

## Slide 14: Development Framework
Mesmerizer
  Software infrastructure for event-based systems development
    Mesmerizer applications can be tested in emulation and deployed in production
    Applications consists of a set of components
  Based on Google’s Guice
    Injection framework
  Event-Driven Runtime
    Emulation: emulated network interactions, DES scheduler
    Deployment: remote event interactions, concurrent event scheduler
  Components written in:
    Java, Python and Scala

## Slide 15: Emulation
Emulation allows for fast debugging and large scale evaluation of the application
Sequential runtime in emulation
  Reproducibility of execution
Network interactions
  Bandwidth allocation dynamics
    Transfers with different/variable priority
  Network Address Translation behavior
  Delays
  Hierarchical Network topology
    AS/ISP/LAN

## Slide 16: Bandwidth emulation
Flow-level bandwidth emulation
  Modeling the transfer as whole (flow) rather than datagrams
  Viable trade-off between accuracy and scalability
  Emulates the transfer as a fixed rate bandwidth allocation on the sender and receiver
  The duration of the flow is the emulation target
  Ripple effect: cascade of allocation and de-allocation events
MsgA

## Slide 17: How to build a peer-to-peer software?
Development
Framework
Money and Time
Network Library
Services
Algorithm
Design and Implementation
Testing

## Slide 18: Network library
P2P Sockets
  Socket-like abstraction library for peer-to-peer applications
    Same interface as the emulated network library
  UDP-based
  Implemented in Java NIO for portability
  State of the art NAT Traversal
  Flow Control and Reliability (as TCP)
  Variable and dynamic transfer priority
    Inter-Protocol / Intra-Protocol

## Slide 19: NAT Problem
na
p1
p2
nb
v1
v2
u1
u2
NAT Box
NAT Box
ux Public endpoint (IP:Port)
vx Private endpoint (IP:Port)
u3
u4
v3
v4
Network Address Translators prevent direct communication between peers in different private networks
Notes: What to describe? Introduce the relay?

## Slide 20: NAT Traversal – Model
We classify NAT Types as Set T of three Policies:
  Mapping (3) [EI,HD,PD]
    “When a new port is opened by the NAT”
  Allocation (3) [PP,PC,R]
    “Which” port number is used
  Filtering (3) [EI,HD,PD]
    “How” the open port can exploited
We claim that Traversal, i.e. hole punching, has to be carried out by considering combinations of all 27 types
  Which leaves 378 possible combinations
    27 possible NAT Types

## Slide 21: NAT combinations table
80% of all combinations are traversable

## Slide 22: NAT Traversal
Experimental results:
  ~4800 peers located in Sweden
  “Open”/not natted peers: 18.1%
  Average connectivity probability
    Direct both ways all-to-all: 85%
    One-way: 8%
    Direct both ways excluding not supported types/one-way: 92%
  Average connection establishment time: 1.8 seconds
  NAT Types observed 18 over 27

## Slide 23: Traffic Prioritization - DTL
Different congestion control mechanisms for traffic prioritization
Lower than best effort priority
Background traffic
Same priority as TCP or higher
Urgent traffic
Delay based
Packet-loss based
Notes: - Goal of the congestion control

## Slide 24: Traffic Prioritization
LEDBAT as congestion control:
  Maximizes throughput
  Fast initial ramp-up
  Shares bottleneck equally with other LEDBAT flows
  Minimizes latency introduced on other traffic
Unfortunately tweaking LEDBAT parameters does not lead to a corresponding degree of aggressiveness
  Delay-based is good for politeness, not for aggressiveness
Runtime switch congestion control from a delay-based algorithm (LEDBAT) to a packet-loss one (MulTCP)
  Without re-establishing the connection!

## Slide 25: Traffic Prioritization
LEDBAT
MulTCP

## Slide 26: How to build a peer-to-peer software?
Development
Framework
Money and Time
Network Library
Services
Algorithm
Design and Implementation
Testing

## Slide 27: Services

## Slide 28: How to build a peer-to-peer software?
Development
Framework
Money and Time
Network Library
Services
Algorithm
Design and Implementation
Testing

## Slide 29: Peer2View
Requirement: support HTTP-based streaming with adaptive bitrate
  Encoder provides:
    X video and Y audio bitrates for same stream
  Media server appears normal HTTP server
  Player pulls fragments and decides:
    Pace of requests
    Buffering time and length
    Quality to reproduce, depending on:
      CPU load
      Bandwidth available
      Rendering capabilities
    Requests for fragments are totally uncorrelated between each others
    Heuristics behavior cumbersome to predict
CDN
Encoder
and
Media Server
HTTP GET
Publish
Player

## Slide 30: Peer2View
Approach to the problem:
  Peer-To-Peer caching
    Overlay network seen as a cache for content fragments
  When player requests a fragment:
    Cache hit (neighbors have fragment): retrieve from peers as fast as possible
    Cache miss: retrieve from the CDN
  This approach allows us to provide quality of user experience (QoE) comparable to the CDN
    We strive not to interfere with heuristics of the player

## Slide 31: Peer2View Overlay
Mesh-based overlay network
  Place peers with higher bandwidth at the center of the gradient
  Peer prefers neighbors that are requesting with the same delay from the source
  Adapt neighbors choice to current bitrate
  Peers with higher bandwidth capacity bubble up closer to the center by pre-fetching
    Requesting fragments ahead of time
  We use prioritization of traffic for prefetching
    +80% P2P transfers happen using LEDBAT
      Politeness towards other applications
Notes: Introduce delays?

## Slide 32
Minimize amount of CDN pre-fetched data
Maximize amount of P2P pre-fetched data
Minimize the amount of data entering each site
Main Site
Secondary
site
Secondary
site
The Corporate Live Streaming overlay
Secondary
site
gateway
CDN

## Slide 33: How to build a peer-to-peer software?
Development
Framework
Money and Time
Network Library
Services
Algorithm
Design and Implementation
Testing

## Slide 34: Testing
Test1 multi-bitrate
Test2 single bitrate
DEMO TIME!

## Slide 35: Single Bitrate Results

## Slide 36: Multi Bitrate Results

## Slide 37: Testing Corporate
Corporate live stream only CDN
Corporate live stream P2P

## Slide 38
Thanks